## Slide 1: UT Robomasters – Supercap Power Stage Modeling
Supercap Technical Lead: Egan Wang (ew23776)
Contributing Members: []
If you can see this, get your butt to work on disturbance rejection and robustness modeling so I can put your name on here

## Slide 2: Overview of Topology
H-Bridge Converter
4 switches
2 half-bridges
Full-bridge analogue to buck converter
Voltage across switched nodes can be +Vg, 0, or +Vg
+Vg
+
-
0
+
-
0
+
-
-Vg
+
-
1 high, 2 low
1 high, 2 high
1 low, 2 low
1 low, 2 high
Possible Voltages

## Slide 3: Duty Cycle Control
Half-bridges 1 and 2 are independent
Both high and both low result in 0 voltage across switch nodes
Duty ratios <2.5% and >97.5% are risky
H-bridge topology allows finer control
Control scheme shown on right
Duty cycle “seen” across switch nodes labelled as M(t)
Half-bridge 1
Half-bridge 2
doff(t)
doff(t)
Halfway point
Half-bridge 1 duty ratio: 0.5 + doff(t)
Half-bridge 2 duty ratio: 0.5 – doff(t)
Duty cycle “seen” by inductive tank: 2*doff(t)
Scope Reading

## Slide 4: Transformer Equivalent
Use SRA analysis and derive KCL- and KVL-like equations
Convert into loops and create ideal transformer model of circuit with gain 1:M(t)
Transformer model will be useful for reflection
Ideal Transformer Model
Voltage/Current Source Model

## Slide 5: Capacitor Feed-Forward Correction
Split the voltage source on the right into a Vc(t) component and remainder
Remainder voltage has to be equal to voltage across RL branch
Current is conserved - take note of the current/voltage behavior of the transformer
“Cut out” the capacitor and focus on the RL branch
Even though Vc(t) is time-variant, it changes very slowly and can be treated as constant
Remember to adjust the voltage source on the left side to compensate – reflect the new voltage source by dividing by M(t)
Separated Voltages
Isolated RL Branch

## Slide 6: Battery Current Reflection
Reflect the voltage source across the transformer
In previous diagram, this is basically already done
Battery current needs to be scaled by turns ratio
We have our toy model!
Write the KVL equation*:
*before you ask, yes, this calculation ignores the term that appears when doing the product rule for . It is possible to account for this by doing another pair of transformer voltage/current reflections, but this presentation is long enough anyway, and the term can be concluded to be negligible. Consider it an exercise for the reader, if you will.
IRL(t) = Ibat(t)/M(t)
Complete Toy Model

## Slide 7: Algebraic Manipulation & Linearization
From the equation:
Multiply by M(t):
This is quite the nasty equation. It has quadratic terms and a derivative. Let’s define a new variable for the LHS of the equation,
labelled MT(t) due to being roughly equivalent to the “transformer reflection” of the voltage gain M(t).
We complete the square and rewrite:
We can then define an auxiliary variable:
Rewrite the KVL equation:
By encapsulating the quadratic term within a new variable, we now have only additions, scalar multiplications, and derivatives – the equation is linear! We can now convert to s-domain:
Rewrite as a transfer function:
We have a proper transfer function now!

## Slide 8: Overall System Design – FF+PI
We go back to our definition of MT(t):
Solve for M(t):
We will be using the solution with both terms added. (The subtractive solution produces identical behavior. Proof is left as exercise to the reader.)
We can thus design our system as a linear black box composed of the linearization above combined with the physical circuitry.
Linearization + Circuit

## Slide 9: Alternative Design – PI2 Control
Math trick of defining auxiliary variable can be done earlier
No need to split apart voltage source on right side of transformer
Reflect battery current to right side once again
New toy model appears analogous to the one in the FF+PI model
Write new KVL loop equation*:
*Remember that caveat in small print from before? Exercise for the reader: can we ignore this imperfection in our calculus now?
Singular RLC Branch
IRL(t) = Ibat(t)/M(t)
Complete Toy Model

## Slide 10: PI2 Control Linearization
From the equation:
Multiply by M(t):
Our algebra trick is a lot simpler now, and we don’t need to complete the square or define a new auxiliary variable:
Our KVL equation is now:
Converting to s-domain:
Rewrite as a transfer function:
A little messier, but this is once again a proper transfer function. Note the factor of s in the numerator.
Once again, we can combine the MT(t) to M(t) transformation and the electrical circuitry together and treat it as a singular linear system.
While I was able to skip over many steps since the approach is similar, this idea of PI2 control seems to be significantly simpler, even if the transfer function looks more complicated. So why not use this method? Let’s test them out…

## Slide 11: PLECS Analysis: Toy Models
Toy Model Simulation as of Making These Slides
In GitHub repository, under Sims_and_Design folder
In case you didn’t know yet, this is what everything is about
Power Stage Simulation - Toy Model.plecs
Message me (Egan) if you don’t understand a section of this model

## Slide 12: Time-Domain Analysis
Constant Target Current
FF+PI performance is in green
PI2 performance is in red
You can’t see it here, but the FF+PI current waveform is overlapping the target current