## Slide 1: UT Robomasters – Supercap System
Egan Wang (ew23776)
Presented 2/10/2026

## Slide 2: Power OR-ing
Power
Time
90W
Objectives:
Draw excess power from battery in low-load periods
Provide supplementary power to robot during high-load periods
Avoid exceeding 90W power budget

## Slide 3: Supercaps
598-DSF117Q3R0
0-3V
110F
x4
Objectives:
Draw excess power from battery in low-load periods
Provide supplementary power to robot during high-load periods
Avoid exceeding 90W power budget

## Slide 4: General Design & Problem Statement
Can directly control: duty cycle
Want to control: current coming from battery, set constant
Inputs: voltages, currents
Problem Statement

## Slide 5: Converter Design – “Full-bridge Buck Converter”
Voltage gain of 2D-1 when operated as shown in diagram
Avoids extreme duty cycles for conversion from 22-26V to 0-3V
Should be bidirectional

## Slide 6: Controls Design
Assumes converter to be ideal transformer
Closed-loop system to set battery current equal to reference calculated using 90W power budget and battery voltage measurement
Specific design of compensator still under development

## Slide 7: Kalman Filtering – Current Sensing
Create linearized model of circuit to calculate supercap voltage and input current
Reduce noise of input measurements
Requires profiling to determine if useful